## Slide 1: The Memory Hierarchy CS154, Autumn 2019, Prof Chien Intro to Computer Systems Book Sections 6.1-6.3

## Slide 2: What Have We Covered So Far?
Physics
Devices
Circuits
Gates
Register-Transfer Level
Microarchitecture
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Programming Language
Algorithm
Application
Register-Transfer Level
Notes: Interface between SW and HW

## Slide 3: ISA / Architecture Topics
Machine representation of numbers
ISA: interface (state + methods) between SW & HW
  Architecture state
  Basic Assembly
  Higher-level language constructs in assembly
    Functions
    Arrays, structs, and unions

## Slide 4: Foundations: Software View of Architecture State
Data
Instructions
CPU
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “EIP” (IA32) or “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
PC
Registers
Memory
Object Code
Program Data
OS Data
Addresses
Stack
Condition
Codes
  Memory
    Byte addressable array
    Code, user data, (some) OS data
    Includes stack used to support procedures
ALU
Notes: Introduce this new view of “memory”

## Slide 5: Foundations: Assembly (“Methods” to Change Architecture State)
Can you recognize a loop?
Can you recognize pointer access?
Can you recognize a loop through an array?
Can you visualize and articulate how the instructions (methods) that make up the loop affect the memory (state) of the system?
Do you understand how the stack tracks function calls?
If the answer is no for any of these questions, seek help:
  On Piazza
  From Profs, TAs, and each other

## Slide 6: Lecture Goals
This week
Microarchitecture
Today
  Motivate need to understand memory system
  Intro to memory hierarchy
Physics
Devices
Circuits
Gates
Register-Transfer Level
Microarchitecture
Instruction Set Architecture
Operating System/Virtual Machines
Programming Language
Algorithm
Application
Register-Transfer Level

## Slide 7: Some numbers
Instruction Type | Frequency
Memory  Register Move | 22%
Conditional Branch | 20%
Compare | 16%
Register  Memory Move | 12%
Add | 8%
And | 6%
Sub | 5%
Register  Register Move | 4%
Function call | 1%
Function return | 1%
Total | 96%
From H&P: Computer Architecture a Quantitative Approach
> 34% of instructions access data memory!
100% of instructions are stored in instruction memory!

## Slide 8: Elements of Program Performance
Mem Ops x Mem Time
ALU Ops x ALU Time
+ Cond Ops x Cond Time
Total Time
The time of any operation is the time to access instruction memory + perform the operation (which can be another memory access)
The time of a memory operation is the time to access data memory plus access instruction memory
Notes: Hardware optimized to execute next instruction in memory

## Slide 9: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
SSD
Disk

## Slide 10: Synthesize This
> 34% of instructions access data memory
100% of instructions access instruction memory
Memory is many orders of magnitude slower than the processor
  For example: Four-issue 2 GHz superscalar accessing 100 ns DRAM could execute 800 instructions during the time for one memory access!
These numbers don’t make sense

## Slide 11: There must be a way to speed up memory access!

## Slide 12: Why Are Memories Slow in the First Place?
Not all memories are slow
But, bigger means slower  Fundamental Tradeoff
  Technology differences
    Hard disk (slow) vs. SSD vs. DRAM vs. SRAM (fast)
  Just physics
    Signals in longer wires take longer to travel
Notes:     Slower technologies are cheaper, so they can be made bigger while are still affordable

## Slide 13: Key Idea: Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 14: Memory Hierarchy
Capacity: Register << Cache << DRAM
Speed: Register >> Cache >> DRAM
On a data access:
  if data is in fast memory -> low-latency access (to cache or register)
  if data is not in fast memory -> long-latency access to DRAM
Small Fast
Memory
(Cache)
Processor
Big Slow
Memory
(DRAM)
Notes: Most of what a program needs would be from the DRAM (let’s focus on this part)

## Slide 15: Why Does Memory Hierarchy Work?
Memory hierarchies only work if …
The small, fast memory actually stores data that is used/re-used by the processor at a given time
  Do they???

## Slide 16: Locality!
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality

## Slide 17: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 18: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 19: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: which of the following functions has good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 20: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}

## Slide 21: Not all operations are created equal
Instructions between registers are fast
Accessing memory is several orders of magnitude slower
One cycle ~1ns

## Slide 22: Quantitative Approach to Computer Architecture
Distribution of x86 data access patterns
A lot of memory access
  > 35% of instructions read data from memory!
  > 20% write data to memory!
The time of any operation is the time to access instruction memory + perform the operation (which can be another memory access)
https://www.strchr.com/x86_machine_code_statistics

## Slide 23
CPU Core (incl L1, L2), L3, and DRAM
18 Billion Skylake18C Server
DRAM BANKS

## Slide 24: Memory Hierarchy in a Modern System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 25: Synthesize (Again)
Fast (more expensive) memories must be small
Large (cheaper) memories must be slow
Therefore, we cannot make all memory fast and we cannot fit all our data in fast memory simultaneously
However…
Programs exhibit locality
  Some subset of memory is accessed repeatedly (temporal locality)
  Subsequent memory access are likely to be near previous ones (spatial locality)
Therefore…
KEY IDEA: Memory hierarchy