## Slide 1: Exam I Review CS 154: Intro to Computer Systems Prof Chien Lecture 14

## Slide 2: Exam 1 Logistics
Covers materials through Today’s Lecture, Lecture #14 (Review)
November 4th, Monday, 7pm-8:30pm, KPTC (Kersten Physics Teaching Center) Room 106
Exam Logistics – closed everything
  Can bring one handwritten sheet of paper
  x86 instruction list will be on the exam paper
  https://www.classes.cs.uchicago.edu/current/15400-1/154-exam1-cheatsheet.pdf
Review Session, Saturday 3-5pm, Crerar 346
SDS students only: see email from Daniar Kurniawan (daniar@uchicago.edu)

## Slide 3: Exam I Topics
Representation of Numbers
Integer Arithmetic
What is Architecture
Basic x86-64 instructions
Control Flow
Procedures
Arrays, Structs, Unions
Memory Hierarchy and Caching

## Slide 4: Memory Organization
Addresses specify byte locations
  Address of first byte in word
  Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
0000
0008

## Slide 5: Byte Ordering
How should bytes be ordered in memory?
  Little Endian: Least significant byte has lowest address
  Big Endian: Least significant byte has highest address
0x00
0x01
0x02
0x03
01
23
45
67
0x00
0x01
0x02
0x03
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01
int x = 0x01234567
0x00
0x01
0x02
0x03
01
23
45
67
0x00
0x01
0x02
0x03
67
45
23
01
Big Endian
Little Endian
01
23
45
67
23
01
67
45
short a[] = {0x0123, 0x4567}
a[0] = 0x0123
a[0] = 0x0123
((char*)a)[1] = 0x23
((char*)a)[1] = 0x01

## Slide 6: Encoding Integers
Sign Bit
  For two’s complement, most significant bit indicates sign
    0 for nonnegative
    1 for negative
  But it is NOT the case that changing the sign bit merely changes the sign of the represented value
Unsigned
Two’s Complement
“Sign” Bit

## Slide 7: Bits, Bytes & Integers
Know how to do basic bit operations
  Shifting, addition, negation, and, or, xor, etc.
If you have w bits
  What are the largest/smallest representable signed numbers?
  What are the largest/smallest representable unsigned numbers?
  What happens to the bits when casting signed to unsigned (and vice versa)?
Distinguish between logical and bitwise operators (e.g., & vs &&)
When does (signed, unsigned) overflow happen?
Bit-level behavior is the same for signed and unsigned.
Notes: Arithmetic right shift never changes the sign
However, left shift may change the sign

## Slide 8: Computer Architecture
Hardware
(Processor + Memory)
The architecture is the
interface
between software and hardware
State - contents of memory
(Note: different architectures may have different kinds of memory)
Methods - change memory
imull
xorl
movq
leaq

## Slide 9: Instruction Set Elements
Operations
Condition codes and conditional jumps
Addressing modes for Memory
Procedure call/return
+ relationship to C source code

## Slide 10: Examples
sub a, b
Mem[b] = Mem[b] - Mem[a];
PC = next instruction;
Is this single-instruction ISA enough?
jmpg a, b, c
PC = c, if and only if Mem[b] > Mem[a]
Is this single-instruction ISA enough?

## Slide 11: Software View of Architecture State
Data
Instructions
CPU
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called RIP in x86-64
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
PC
Registers
Memory
Object Code
Program Data
OS Data
Addresses
Stack
Condition
Codes
  Memory
    Byte addressable array
    Code, user data, (some) OS data
    Includes stack used to support procedures
ALU
Heap
Notes: %rsp is architecture or microarchitecture?
Memory address?
# of cache sets in a cache?

## Slide 12: A Very Simple Program (1+2 = 3, stored at 0x11c)
0x01
0x02
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
%rax
%rdx
%rcx
%rbx
%rsi
%rdi
%rsp
%rbp
0x104
movq (%rax), %rbx
addq (%rdx), %rbx
movq %rbx, (%rcx)
0x124
0x120
0x11c
ALU
Notes: Now let’s show where xp and yp point too …

## Slide 13: A Very Simple Program (1+2 = 3)
0x01
0x02
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
%rax
%rdx
%rcx
%rbx
%rsi
%rdi
%rsp
%rbp
0x104
0x124
0x120
0x11c
0x01
ALU
movq (%rax), %rbx
addq (%rdx), %rbx
movq %rbx, (%rcx)
Notes: Now let’s show where xp and yp point too …

## Slide 14: A Very Simple Program (1+2 = 3)
0x01
0x02
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
%rax
%rdx
%rcx
%rbx
%rsi
%rdi
%rsp
%rbp
0x104
0x124
0x120
0x11c
0x03
ALU
movq (%rax), %rbx
addq (%rdx), %rbx
movq %rbx, (%rcx)
Notes: Now let’s show where xp and yp point too …

## Slide 15: A Very Simple Program (1+2 = 3)
0x01
0x02
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
%rax
%rdx
%rcx
%rbx
%rsi
%rdi
%rsp
%rbp
0x104
0x124
0x120
0x11c
0x03
ALU
movq (%rax), %rbx
addq (%rdx), %rbx
movq %rbx, (%rcx)
0x03
Notes: Now let’s show where xp and yp point too …

## Slide 16: “For” loop example
int array_mul(
int* A, int* B, long n){
int val = 0;
int i;
for (i = 0; i != n; i++){
val += A[i]*B[i];
}
return val;
}
array_mul:
movq $0, %rax
movq $0, %rcx
jmp .L2
.L3:
movl (%rdi,%rcx,4), %r8d
imull (%rsi,%rcx,4), %r8d
addl %r8d, %eax
addq $1, %rcx
.L2:
cmpq %rcx, %rdx
jne .L3
.L4:
ret

## Slide 17: Assembly: Basics, Loops
Recognize common assembly instructions
Understand how different control flow is turned into assembly
  For, while, if-else, etc
Be very comfortable with pointers and dereferencing
  The use of parens in mov commands.
    %rax vs. (%rax)
  The options for memory addressing modes:
    D(Rb, Ri, S)
  leaq vs. movq
Notes: leaq (%rdi, %rdi, 2), %rax
vs.
movq (%rdi, %rdi, 2), %rax

## Slide 18: x86-64/Linux Stack Frame
Caller Stack Frame
  Return address
    Pushed by call instruction
  Arguments for this call (optional)
Callee Stack Frame
  Saved register context
  Local variables If can’t keep in registers
  Arguments for function about to call (optional)
Return Addr
Saved
Registers
+
Local
Variables
Argument build
(Optional)
Argument build
(Optional)
Caller
Frame
Stack pointer
%rsp
Callee
Frame

## Slide 19: x86-64 Linux Register Usage #1
Carnegie Mellon
%rax
  Return value
  Also caller-saved
  Can be modified by procedure
%rdi, ..., %r9
  Arguments
  Also caller-saved
  Can be modified by procedure
%r10, %r11
  Caller-saved
  Can be modified by procedure
%rax
%rdx
%rcx
Return value
%r8
%r9
%r10
%r11
%rdi
%rsi
Arguments
Caller-saved
temporaries

## Slide 20: x86-64 Linux Register Usage #2
Carnegie Mellon
%rbx, %r12, %r13, %r14 , %rbp
  Callee-saved
  Callee must save & restore
%rsp
  Special form of callee save
  Restored to original value upon exit from procedure
%rbx
%rsp
Callee-saved
Temporaries
Special
%rbp
%r12
%r13
%r14

## Slide 21: Assembly – Stack
How arguments are passed to a function?
How does a function pass the return value?
How these instructions modify stack
  call
  ret
  pop
  push

## Slide 22: Array Access
  Understand how in assembly, a logical 2D array is implement as a 1D array, using the width of the array as a multiplier for access

## Slide 23: Memory Hierarchy and Locality
Temporal Locality:
If a location is
referenced it is likely
to be referenced again
in the near future
Spatial Locality:
If a location is
referenced it is likely
that locations near it
will be referenced in
the near future
Cache: A smaller, faster memory that acts as a staging area for a subset of the data in a larger, slower memory (DRAM)
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Notes: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 24: Cache Basics
E = 2e blocks per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any block in set has matching tag
Yes + block valid: hit
Locate data starting at offset
address of word: m bits

## Slide 25: Cache Basics
Block Placement:
  Where can a block be placed in the cache?
Block Identification:
  How a block is found if it is in the cache?
Block Replacement:
  Which block should be replaced on a miss?
Write Strategy:
  What happens on a write?
First example of microarchitecture
  What is microarchitecture and how is it different from architecture (ISA)?

## Slide 26: Filter Example
int filter[4];
int apply_filter(int* in) {
int i;
int x = 0;
for(i = 0; i < 4; i++) {
x += in[i]*filter[i];
}
return x;
}
apply_filter:
movq $0, %rax
movq $0, %rdx
.L2:
movl (%rdi,%rdx,4), %ecx
imull filter(,%rdx,4), %ecx
addl %ecx, %eax
addq $1, %rdx
cmpq $4, %rdx
jne .L2
ret

## Slide 27: Address Trace
0x00
0x04
0x08
0x0C
Address
%rdi
0x10
filter
%rdx i | filter(,%rdx,4) &filter[i] | (%rbx,%rdx,4) &in[i]
0 | 0x00 | 0x10
1 | 0x04 | 0x14
2 | 0x08 | 0x18
3 | 0x0C | 0x1C
movl (%rdi,%rdx,4), %ecx
imull filter(,%rdx,4), %ecx
0x10
0x14
0x18
0x1C

## Slide 28: Cache Performance Analysis
Derive memory traces from assembly
  You need to know assembly, recognize pointer references (both read and write), recognize loops, function calls, etc.
For each access, hit or miss?
  You need to know the basics of caching
If cache performance is not good (e.g., low hit rate), how can you make it better?
  You need to know the tradeoffs of different cache designs: bigger cache? Higher associativity? Larger block size?

## Slide 29: Exam I Topics
Representation of Numbers
Integer Arithmetic
What is Architecture
Basic x86-64 instructions
Control Flow
Procedures
Arrays, Structs, Unions
Memory Hierarchy and Caching